## Slide 1: Spatial Data Analytics with Classical Data Mining and Machine Learning Algorithms
Yao-Yi Chiang
Computer Science and Engineering
University of Minnesota
yaoyi@umn.edu
CC-BY
Attribution

## Slide 2: Mining Public Datasets for Modeling Intra-City PM2.5 Concentrations at a Fine Spatial Resolution
A motivating example
Lin Y., Pan F., Chiang Y.-Y., Stripelis D., Ambite J. L., Eckel S. P., and Habre R. (November 2017) Mining public datasets for modeling intra-city PM2.5 concentrations at a fine spatial resolution. ACM SIGSPATIAL.

## Slide 3: Air Pollution is a Global Problem

## Slide 4: Air Pollutant: PM2.5 and PM10
PM2.5 : fine inhalable particles, with diameters that are generally 2.5 micrometers and smaller
United States Environmental Protection Agency

## Slide 5: Air Quality Index
AQI: air quality index computed from a piecewise linear function of the pollutant concentration (e.g., 12.0 micrograms per cubic meter is 50 AQI for PM2.5).

## Slide 6: Limited Air Quality Observations
Central LA
  Monitoring stations are usually sparse – 12 stations for PM2.5 in Los Angeles

## Slide 7: Nearby locations would have similar air quality
Tobler's 1st law of geography:
Spatial interpolation? IDW?
Vandecasteele & Devillers, Improving volunteered geographic data quality using semantic similarity measurements
“all things are related, but nearby things are more related than distant things” Tobler – 1970

## Slide 8: Typical Air Quality Prediction Result (AirNow)
https://www.airnow.gov/?reportingArea=Central%20LA%20CO&stateCode=CA

## Slide 9: Inverse Distance Weighting
Why are the results so smooth over space?
Recall IDW:
Dec 2016
Jan 2017

## Slide 10: Machine Learning Methods
Some prediction variations in space, e.g., the road network is obvious
“Powered by proprietary algorithms,
strict QA & machine learning.”

## Slide 11: Existing Work for Air Quality Modeling
The built environment has a strong impact on air quality but how?
?

## Slide 12: Land-use Regression Models (LUR)
Expert-selected &
Area-specific
e.g., PM2.5 concentrations is high near 500 meters of highways in Los Angeles
Source: Liu et al., 2016
Taiwan

## Slide 13: LUR Limitations
Experts are expensive
Do not scale well for predictions at various spatial and temporal resolutions
Sometimes rely heavily on datasets that are not easy to obtain
  e.g., traffic
Source: Liu et al., 2016
Can we do better?

## Slide 14: JonSnow: Data-Driven Air Quality Prediction at Fine-Spatial Scale
  Problem
    Given some sensors and their locations, predicting air quality for locations that do not have a sensor
  Hypothesis
    Similar environments should have a similar air quality

## Slide 15: Data Collection
PRISMS-DSCIC – A scalable data integration and analysis architecture
Integration and Storage
Data Sources / Sensors
Streaming
Analytics
General Data Processing

## Slide 16: Data Sources – I
AQS (Air Quality System) Data
  Hourly PM2.5 AQI from 12 monitoring stations in the Los Angeles Area from 2016-10-30 00:00:00 to 2017-08-31 23:00:00
Sample data
Monitoring Station | Timestamp | PM2.5 AQI
San Gabriel Mts | 2017-03-04 12:00:00 | 44
San Gabriel Mts | 2017-03-04 13:00:00 | 54
Central LA | 2017-03-04 12:00:00 | 60
Central LA | 2017-03-04 13:00:00 | 68
San Gabriel Mts
Central LA

## Slide 17: Data Sources – II
Geographic Features - OpenStreetMap (OSM)
  Land uses (67,972 polygons), Roads (544,142 lines), Water areas (11,207 polygons), Buildings (2,971,349 points), Aeroways (962 lines), etc.
  Each geographic category contains various feature subtypes
    e.g., subtypes for “Buildings”: commercial, apartment, house, industrial, school, etc.

## Slide 18: Recall: JonSnow: Data-Driven Air Quality Prediction at Fine-Spatial Scale
  Problem
    Given some sensors and their locations, predicting air quality for locations that do not have a sensor
  Hypothesis
    Similar environments should have a similar air quality

## Slide 19: Approach Overview
Similar environments should have a similar air quality
  How to quantify “similar air quality”
    Clustering of air quality measurements
    K-Means, hierarchical clustering, dimension reduction
  How to quantify ”similar environments”
    Train an interpretable machine learning model using geographical context to predict whether two locations would have “similar air quality”
    Random Forest
Pedestrian
100m
0.1
Motorway
100m
5.28
Apartment
200m
2
Factory
200m
0.3
…
Pedestrian
100m
0.0
Monitoring Station 1
Motorway
100m
3.27
Apartment
200m
0.041
Factory
200m
0.432
…
Monitoring Station 0

## Slide 20: Required Technologies
Clustering
  K-Means, Hierarchical Clustering
Dimension Reduction
  SVD (Singular Value Decomposition)
Interpretable Machine Learning Method
  Random Forest

## Slide 21: Step 1. Grouping Stations based on their PM2.5 AQIs
    To identify the monitoring stations that have similar temporal pattern on PM2.5 AQIs
    These monitoring stations should have a similar environment.
Notes: Feature selection – we don’t know which variable in the built environment affect PM2.5 and from what distance

## Slide 22: Similar Temporal Pattern

## Slide 23: K-means Clustering
Input: time-series observations at each station
Output: clusters of stations having a similar temporal pattern

## Slide 24: K-means Clustering
    Recall: Hypothesis
    Similar environments should have a similar air quality
    Stations in the same cluster have a similar temporal pattern
    How to quantify “similar environment”
      what specific geographic feature types (e.g., primary roads, industrial areas, parks)
      from what distance have the most impact on the clustering result?
Output: clusters of stations having a similar temporal pattern

## Slide 25: Step 2. Generating Geographic Abstraction
[23, 30, 43, 200]
Length of line features
  e.g., Roads, Aeroways
 | 100m | 200m
Pedestrian | 23 | 43
Motorway | 30 | 200
Example Roads

## Slide 26: Step 2. Generating Geographic Abstraction
[2, 0, 8, 3]
Count of point features
  e.g., Buildings
 | 100m | 200m
Apartment | 2 | 8
Factory | 0 | 3
Example Buildings

## Slide 27: Step 2. Generating Geographic Abstraction
Area of polygon features
e.g., Land uses, Water areas
 | 100m | 200m
Park | 500 | 950
Industrial | 0 | 740
Example Land uses
[500, 0, 950, 740]

## Slide 28: Step 2. Generating Geographic Abstraction
Generating a large vector for each monitoring station
In practice, we creates buffers from 100 meters to 3,000 meters with an interval of 100 meters
  3,500+ components in a vector
Pedestrian
100m
23
Distance to Ocean
4000
Monitoring Station X
Motorway
100m
30
Pedestrian
200m
43
Motorway
200m
200
Park
100m
500
Industrial
100m
0
Apartment
100m
2
Factory
100m
0
Apartment
200m
8
Factory
200m
3
Park
200m
950
Industrial
200m
740

## Slide 29: How to quantify “similar environment”
Geographic abstraction
Clustering result
?

## Slide 30: Step 3. Computing Feature Importance
  Training a random forest model to
    predict cluster label using the geographic context
      each feature component represents a geographic feature type within certain distance
    quantify the impact of each feature component
Temporal pattern cluster
Cluster 1
Cluster 1
Cluster 2
Cluster 2
Pedestrian
100m
23
Monitoring Station 1
Motorway
100m
30
Apartment
200m
2
Factory
200m
3
…
Pedestrian
100m
10
Monitoring Station 2
Motorway
100m
25
Apartment
200m
1
Factory
200m
3
…
Pedestrian
100m
56
Monitoring Station 3
Motorway
100m
5
Apartment
200m
7
Factory
200m
0
…
Pedestrian
100m
67
Monitoring Station 4
Motorway
100m
10
Apartment
200m
8
Factory
200m
0
…

## Slide 31: Step 3. Generating Geo-context
  Multiplying each geographic abstraction value by its feature importance to generate geo-context
Geo-feature | Importance
Pedestrian 100m | 0.000
Motorway 100m | 0.109
… | …
Apartment 200m | 0.041
Factory 200m | 0.144
… | …
Total | 1.0
Pedestrian
100m
23
Monitoring Station 1
(Geographic Abstraction)
Motorway
100m
30
Apartment
200m
2
Factory
200m
3
…
Pedestrian
100m
0.0
Monitoring Station 1
(Geo-context)
Motorway
100m
3.27
Apartment
200m
0.041
Factory
200m
0.432
…
Example of Importance

## Slide 32: Step 3. Geo-context
    Geo-context is an updated vector from geo-abstract for describing
      how each feature type within a certain distance (a feature component) in Geographic Abstraction affects the Temporal Pattern (PM2.5 AQI)
    Reward important (relevant) features and penalize others
Pedestrian
100m
23
Monitoring Station 1
(Geographic Abstraction)
Motorway
100m
30
Apartment
200m
2
Factory
200m
3
…
Pedestrian
100m
0.0
Monitoring Station 1
(Geo-context)
Motorway
100m
3.27
Apartment
200m
0.041
Factory
200m
0.432
…

## Slide 33: Step 4. Predicting PM2.5 AQI
Train a regression model to predict PM2.5 AQI for a target location at time T
[Geo-context] for target location
Regression Model
AQI prediction of target location
[Geo-context, AQI] for each monitoring station at time T

## Slide 34: Experiments
Leave-one-out cross-validation method
  Predict PM2.5 AQI for the removed station by using other 11 stations
  Compare our approach with baseline methods
Predicting at a fine scale
  Predict PM2.5 AQI of each point on an 1-mile-apart fishnet covering most of the Los Angeles area (604 points)
  Visualize the fine-scale prediction results

## Slide 35: Experiment & Result – I
Leave-one-out cross-validation method
Tested with three methods on three temporal scales
  Geo-context, Geo-abstraction, IDW (Inverse distance weighting)
  Monthly (7 months), daily (233 days), and hourly (168 hours)
  RMSE - root-mean-square error; MAE - mean absolute error
IDW method
All within 10% error margin; Significant different with 95% confidence (paired t-test)

## Slide 36: Experiment & Result – I (Cont’d)

## Slide 37: Experiment & Result – II
Predicting PM2.5 AQIs at a fine scale
Dec 2016
Dec 2016
Jan 2017
Jan 2017
Geo-context
IDW

## Slide 38: Experiment & Result – II
Predicting PM2.5 AQIs at a fine scale
Dec 2016
Dec 2016
Jan 2017
Jan 2017
Geo-context
IDW

## Slide 39: Experiment & Result – II
Predicting PM2.5 AQIs at a fine scale
Dec 2016
Dec 2016
Jan 2017
Jan 2017
Geo-context
IDW

## Slide 40: Related Work
 | Limitations | Advantages of our method
Spatial interpolation methods, e.g., IDW and Kriging | Not considering neighborhood characteristic | With neighboring geographic features
 | Cannot generate a fine scale result with sparse monitoring stations | Can generate accurate result in a fine scale
Dispersion models | Require detailed data (e.g., building heights and distance between neighboring buildings) | Use easily accessible datasets (OpenStreetMap)
Land-use regression (LUR) methods (e.g., Hoek (2008)) | Rely on expert-selected predictors, including types and spatial radii | Expert-free feature selection

## Slide 41: Summary
A spatial data mining approach to build an accurate model to predict PM2.5 concentrations at a fine scale by
Automated selection of important geographic features without using expert knowledge.

## Slide 42: Additionally, Air Quality Forecasting
Goal
Build a general approach for location-dependent time-series data forecasting
Challenges:
Existing approaches do not handle spatial correlation well
e.g., Auto-Regression Integrated Moving Average (ARIMA), Kalman filtering,
Artificial Neural Network (ANN)
Our approach
  We are building a Diffusion Convolutional Recurrent Neural Network for forecasting location-dependent time series data.
  Continuously forecasting air quality index (AQI) in next 24 hours at a fine scale using data on the PRISMS-DSCIC
Lin, Y., Mago, N., Gao, Y., Li, Y., Chiang, Y.-Y., Shahabi, C., and Ambite, J. L. (November 2018). Exploiting Spatiotemporal Patterns for Accurate Air Quality Forecasting using Deep Learning. In Proceedings of the 26th ACM SIGSPATIAL International Conference on Advances in Geographic Information Systems, pp. 359 – 368, Seattle, WA, USA

## Slide 43: DCRNN – Diffusion Convolutional Recurrent Neural Network
Spatial Dependency Modeling
Use diffusion convolution to learn a function that maps historical graph signal to future graph signal
Temporal Dependency Modeling
Use Recurrent Neural Networks
Graph Construction
Each point in the graph represents the time series at the station
The link between points would be the proximity between stations (e.g., distance, geographic similarity)
Air quality time series
Forecasting result

## Slide 44: Acknowledgements
Gil, Yolanda (Ed.) Introduction to Computational Thinking and Data Science. Available from http://www.datascience4all.org

## Slide 45: These materials are released under a CC-BY License
You are free to:
  Share — copy and redistribute the material in any medium or format
  Adapt — remix, transform, and build upon the material
for any purpose, even commercially.
The licensor cannot revoke these freedoms as long as you follow the license terms.
Under the following terms:
Attribution — You must give appropriate credit, provide a link to the license,
and indicate if changes were made. You may do so in any reasonable manner,
but not in any way that suggests the licensor endorses you or your use.
https://creativecommons.org/licenses/by/2.0/
Please credit as: Chiang, Yao-Yi Introduction to Spatial Artificial Intelligence. Available from https://yaoyichi.github.io/spatial-ai.html
If you use an individual slide, please place the following at the bottom: “Credit: https://yaoyichi.github.io/spatial-ai.html
We welcome your feedback and contributions.
Artwork taken from other sources is acknowledged where it appears.
Artwork that is not acknowledged is by the author.
Credit: http://www.datascience4all.org/